## Slide 1: Load Analysis for Vertical Rescuers
by Alan Sheehan B.E.
Senior Vertical Rescue Trainer
Oberon Unit
New South Wales State Emergency Service

## Slide 2: Why Analyse Loads?
To avoid overloading
To improve rigging skills
Because not all systems are symmetrical!
To understand how rigging affects loads
To find the highest loads in a system
To find the weakest link in a system
To be safer riggers and rescuers
Introduction

## Slide 3: Some Facts about Rope
Rope cannot be used to PUSH
Rope has no significant bending or shear stiffness (except when length approaches the diameter)
Rope can only be used to PULL…
Hence the direction of TENSION in a rope is always along the rope!
Forget the Indian Rope Trick...
Background info...

## Slide 4: Static Equilibrium
We desire rescue systems that are stable, static, do not go anywhere
“For every action, there is an equal and opposite reaction” - Sir Isaac Newton
  So the load on the rope must be balanced by an equal load in the opposite direction
Newton said...
Background info...

## Slide 5: Load Analysis! - How?
Start with the load you know
Draw lines and arrows parallel to the loads
Measure with your hands and fingers
Work step by step through the system
Divide MBL or SWL by the Load to find the Weakest Link
With practice this can be done mentally!
The Procedure

## Slide 6: Start with the Known Load
Consider this Load Sharing Anchor
We know the Load we want to put on the rope
We want to know the loads on the:
  karabiner
  slings
  anchors
Step 1

## Slide 7: Draw the Known Load
Draw an arrow parallel to the known load
Make it ONE HANDSPAN long as shown
This represents 100% of the known load
Feel the force...

## Slide 8: Draw the Directions of the Unknown Loads
Draw lines parallel to the unknown loads (in this case, the slings)
One must start at the head of the arrow, the other at the tail
They must intersect
Step 2

## Slide 9: Draw the “Vectors”
Draw arrowheads on the sides of the triangle to show the direction of the forces (loads)
They must ALL be head to tail
The length of each arrow represents the amount of force (load)
Darth Vector

## Slide 10: Measuring the Unknown Loads
Notice that two fists placed as shown in the photo are the same length as 1 handspan!
So each finger or knuckle is 10%!
Step 3

## Slide 11: Measure the Forces
Use handspans, fistspans and knuckles measure the length of the arrows
Remember the length represents how much force or load!
Have faith, Luke...

## Slide 12: We now know all the loads!
If the load on the rope is 200kgs, the white sling and anchor carries 110kgs, while the green one carries 140kgs.
Just mental arithmetic!
May the force be with you

## Slide 13: We can even check Cross Loading!
Take notice of the orientation of the krab
Draw 2 lines each side of the triangle parallel to the spine of the krab
The distance between is the amount of cross load! 40% in this case.

## Slide 14: Find the Weakest Link
Rope: MBL=3000kgs, Load=200kgs - SF=3000/200=15(>8 so OK).
Sling (doubled): MBL=5333, Load=140kgs - SF=5333/140=38
Krab: MBL=2000kgs, Load=200kgs - SF=2000/200=10(>5 so OK).
Krab Cross Load: MBL=600kgs, Load=80kgs - SF=600/80=7.5! (>5 so OK.)
So the krab is the weakest link and would fail due to cross loading... if overloaded!
Note: SF=8 for rope, SF=5 for hardware used for this example

## Slide 15: …can be applied to any System.
Consider this pulley rigged as a tyrolean
The known load is on the white tape
The rope carries 180% of the load on the tape!

## Slide 16: Angles make the Difference!
Here’s the same tyrolean rig, but with excessive sag to effectively make it a self equalising anchor
Notice the loads are now down to 60% of the known load.

## Slide 17: Redirections
In this case, the known load is on the rope
The load in the rope does not change through the pulley
The more bend in the rope, the more force on the redirection pulley, krab and anchor!

## Slide 18: FAQ
What do we draw with?
  With a finger or stick in the dirt, or a rock or chalk on rock
Do we have to do this all the time?
  No. It’s a tool. Use it when you need it. Practice it, and you’ll be able to do it in your head!
How accurate is this method?
  As accurate as you can draw it!
Any Questions?

## Slide 19: Practice!
With practice this can be done mentally!
Have faith, Luke...
May the force be with you
Newton said...