## Slide 2: Group Members
Arooj Hasssan
Hafsah Parvez
Kiran Shahzadi
Leeena Sarwer
Sadaf Baig

## Slide 3: Group # 07 Topic Packet Switching And Frame Relay

## Slide 4: Packet Switching
Developed in 1970s for long-distance data transmission due to circuit switching limitations.

## Slide 5: Packet vs Circuit Switching
In user/host data connection the line is often idle, so circuit-switching is inefficient
Circuit-switching requires both devices to transmit and receive at the same data rate, limiting interconnection options

## Slide 6: Introduction
Packet Switching refers to protocols in which messages are divided into packets before they are sent. Each packet is then transmitted individually and can even follow different routes to its destination. Once all the packets forming a message arrive at the destination, they are recompiled into the original message.

## Slide 7: Packet Switching Operation
Data are transmitted in short packets. Typically an upper bound on packet size is 1000 octets.
If a station has a longer message to send it breaks it up into a series of small packets. Each packet now contains part of the user's data and some control information.
The control information should at least contain:
  Destination Address
  Source Address
Store and forward - Packets are received, stored briefly (buffered) and past on to the next node

## Slide 8: Advantages
Line efficiency
  Single node to node link can be shared by many packets over time
  Packets queued and transmitted as fast as possible
Data rate conversion
  Each station connects to the local node at its own speed
  Nodes buffer data if required to equalize rates
Packets are accepted even when network is busy
  Delivery may slow down
Priorities can be used

## Slide 9: Switching Technique - Virtual Circuits and Datagrams
Station breaks long message into packets
Packets sent one at a time to the network
Packets handled in two ways
  Datagram
  Virtual circuit
LINK OF PACKET
SWITCHING

## Slide 10: Datagram Packet Switching
In datagram approach each packet is treated independently with no reference to packets that have gone before. No connection is set up.
Packets can take any practical route
Packets may arrive out of order
Packets may go missing
Up to receiver to re-order packets and recover from missing packets
More processing time per packet per node
Robust in the face of link or node failures.

## Slide 11
Packet Switching Datagram Approach

## Slide 12: Virtual Circuit Packet Switching
In the Virtual Circuit approach a pre-planned route is established before any packets are sent.
There is a call set up before the exchange of data (handshake).
All packets follow the same route and therefore arrive in sequence.
Each packet contains a virtual circuit identifier instead of destination address
More set up time
No routing decisions required for each packet - Less routing or processing time
Susceptible to data loss in the face of link or node failure
Clear request to drop circuit
Not a dedicated path

## Slide 13
Packet Switching Virtual Circuit Approach

## Slide 14: Virtual Circuits vs. Datagram
Virtual circuits
  Network can provide sequencing and error control
  Packets are forwarded more quickly
    No routing decisions to make
  Less reliable
    Loss of a node looses all circuits through that node
Datagram
  No call setup phase
    Better if few packets
  More flexible
    Routing can be used to avoid congested parts of the network

## Slide 15: Packet switching - datagrams or virtual circuits
Interface between station and network node
  Connection oriented
    Station requests logical connection (virtual circuit)
    All packets identified as belonging to that connection & sequentially numbered
    Network delivers packets in sequence
    External virtual circuit service
    Different from internal virtual circuit operation
  Connectionless
    Packets handled independently
    External datagram service
    Different from internal datagram operation

## Slide 16: External Virtual Circuit and Datagram Operation

## Slide 17: Internal Virtual Circuit and Datagram Operation

## Slide 18: Frame Relay
Frame Relay is a high-performance WAN protocol that operates at the physical and data link layers of the OSI reference model.
Frame Relay is an example of a packet-switched technology.

## Slide 19: Frame Relay Virtual Circuits
Switched Virtual Circuits
  GSM mobile technology.
Permanent Virtual Circuits
  AIMS technology.

## Slide 20: Congestion Control Mechanisms
Forward Explicit Congestion Notification (FECN)
  part of the Address field in frame header.
  set the value of the frames’ FECN bit to 1.
  flow control may be initiated or ignored.

## Slide 21: Congestion Control Mechanisms
Backward Explicit Congestion Notification (BECN)
  part of the Address field in frame header
  particular path through the network is congested.
  flow control may be initiated, ignored.

## Slide 22: Frame Relay Discard Eligibility
The Discard Eligibility (DE) bit is used to indicate that a frame has lower importance than other frames.
The DE bit is part of the Address field in the Frame Relay frame header.
Value of the DE bit of a frame to 1 to indicate that the frame has lower importance than other frames.

## Slide 23: Frame Relay Error Checking
Frame Relay uses a common error-checking mechanism known as the cyclic redundancy check (CRC).
The CRC compares two calculated values to determine whether errors occurred during the transmission from source to destination.
Reduces network overhead by implementing error checking.

## Slide 24: Frame Relay Frame Formats
There are two frame formats.
  Standard Frame Relay Frame
  LMI Frame Format

## Slide 25: Standard Frame Relay Frame

## Slide 26: LMI Frame Format
Local Management Interface (LMI)
Data Link Connection Identifier (DLCI)
Frame Check Sequence (FCS)

## Slide 27: Frame Relay
Capabilities
  Windowing
  Retransmission

## Slide 28
THANKS