## Slide 1: What is Line Coding?
Line coding is the process of converting binary data, a sequence of bits to a digital signal. For example data, text, numbers, graphical images, audio and video that are stored in computer memory are all sequences of bits.
Mapping of binary information sequence into the digital signal that enters the channel
  Ex. “1” maps to +A square pulse; “0” to –A pulse
Line code selected to meet system requirements:
  Transmitted power: Power consumption = $
  Bit timing: Transitions in signal help timing recovery
  Bandwidth efficiency: Excessive transitions wastes bw
  Low frequency content: Some channels block low frequencies
    long periods of +A or of –A causes signal to “droop”
    Waveform should not have low-frequency content
  Error detection: Ability to detect errors helps
  Complexity/cost: Is code implementable in chip at high speed?

## Slide 2
Line Coding
a. NRZ
0 = low level 1 = high level
b. RZ
0 = low level
1 = transition from low to high at the beginning of the interval and a
transition from high to low in the middle
c. Bi-phase
Manchester coding
0 = transition from high to low in middle of bit interval
1 = transition from low to high in middle of bit interval
(or vice versa)
00 : 11 :
Also known as a self-clocking code.
0
0
1
1

## Slide 3: Line coding examples
NRZ-inverted
(differential
encoding)
1
0
1
0
1
1
0
0
1
Unipolar
NRZ
Bipolar
encoding
Manchester
encoding
Differential
Manchester
encoding
Polar NRZ

## Slide 4: Spectrum of Line codes
Assume 1s & 0s independent & equiprobable
NRZ has high content at low frequencies
Bipolar tightly packed around T/2
Manchester wasteful of bandwidth

## Slide 5: Unipolar & Polar Non-Return-to-Zero (NRZ)
Unipolar NRZ
“1” maps to +A pulse
“0” maps to no pulse
High Average Power
  0.5*A2 +0.5*02=A2/2
Long strings of A or 0
  Poor timing
  Low-frequency content
Simple
Polar NRZ
“1” maps to +A/2 pulse
“0” maps to –A/2 pulse
Better Average Power
  0.5*(A/2)2 +0.5*(-A/2)2=A2/4
Long strings of +A/2 or –A/2
  Poor timing
  Low-frequency content
Simple
1
0
1
0
1
1
0
0
1
Unipolar NRZ
Polar NRZ

## Slide 6: Bipolar Code
Three signal levels: {-A, 0, +A}
“1” maps to +A or –A in alternation
“0” maps to no pulse
  Every +pulse matched by –pulse so little content at low frequencies
String of 1s produces a square wave
  Spectrum centered at T/2
Long string of 0s causes receiver to lose synch
Zero-substitution codes
1
0
1
0
1
1
0
0
1
Bipolar Encoding

## Slide 7: Manchester code & mBnB codes
“1” maps into A/2 first T/2, -A/2 last T/2
“0” maps into -A/2 first T/2, A/2 last T/2
Every interval has transition in middle
  Timing recovery easy
  Uses double the minimum bandwidth
Simple to implement
Used in 10-Mbps Ethernet & other LAN standards
mBnB line code
Maps block of m bits into n bits
Manchester code is 1B2B code
4B5B code used in FDDI LAN
8B10b code used in Gigabit Ethernet
64B66B code used in 10G Ethernet
1
0
1
0
1
1
0
0
1
Manchester Encoding

## Slide 8: Differential Coding
Errors in some systems cause transposition in polarity, +A become –A and vice versa
  All subsequent bits in Polar NRZ coding would be in error
Differential line coding provides robustness to this type of error
“1” mapped into transition in signal level
“0” mapped into no transition in signal level
Same spectrum as NRZ
Errors occur in pairs
Also used with Manchester coding
NRZ-inverted
(differential
encoding)
1
0
1
0
1
1
0
0
1
Differential
Manchester
encoding