## Slide 1
Chapter 5
Analog Transmission

## Slide 2
5.1 Modulation of Digital Data
Digital-to-Analog Conversion
Amplitude Shift Keying (ASK)
Frequency Shift Keying (FSK)
Phase Shift Keying (PSK)
Quadrature Amplitude Modulation
Bit/Baud Comparison

## Slide 3
Figure 5.1 Digital-to-analog modulation
Digital-to-analog conversion is the process of changing one of the characteristics of an analog signal based on the information in digital data.

## Slide 4
Figure 5.2 Types of digital-to-analog modulation

## Slide 5
Bit rate is the number of bits per second. Baud rate is the number of signal units per second. Baud rate is less than or equal to the bit rate.
Note:

## Slide 6
Example 1
An analog signal carries 4 bits in each signal unit. If 1000 signal units are sent per second, find the baud rate and the bit rate
Solution
Baud rate = 1000 bauds per second (baud/s)
Bit rate = 1000 x 4 = 4000 bps

## Slide 7
Example 2
The bit rate of a signal is 3000. If each signal unit carries 6 bits, what is the baud rate?
Solution
Baud rate = 3000 / 6 = 500 baud/s

## Slide 8: Amplitude Shift Keying
The strength of the carrier signal is varied to represent binary 1 or 0.
Both frequency and phase remain constant while the amplitude changes.
Unfortunately ASK transmission is highly susceptible to noise interference.
A popular ASK technique is called on/off keying (OOK).
In OOK one of the bit values is represented by no voltage.
The advantage is a reduction in the amount of energy required to transmit information.

## Slide 9
Figure 5.3 ASK

## Slide 10
Figure 5.4 Relationship between baud rate and bandwidth in ASK

## Slide 11
Example 3
Find the minimum bandwidth for an ASK signal transmitting at 2000 bps. The transmission mode is half-duplex.
Solution
In ASK the baud rate and bit rate are the same. The baud rate is therefore 2000. An ASK signal requires a minimum bandwidth equal to its baud rate. Therefore, the minimum bandwidth is 2000 Hz.

## Slide 12
Example 4
Given a bandwidth of 5000 Hz for an ASK signal, what are the baud rate and bit rate?
Solution
In ASK the baud rate is the same as the bandwidth, which means the baud rate is 5000. But because the baud rate and the bit rate are also the same for ASK, the bit rate is 5000 bps.

## Slide 13
Example 5
Given a bandwidth of 10,000 Hz (1000 to 11,000 Hz), draw the full-duplex ASK diagram of the system. Find the carriers and the bandwidths in each direction. Assume there is no gap between the bands in the two directions.
Solution
For full-duplex ASK, the bandwidth for each direction is
BW = 10000 / 2 = 5000 Hz
The carrier frequencies can be chosen at the middle of each band (see Fig. 5.5).
fc (forward) = 1000 + 5000/2 = 3500 Hz
fc (backward) = 11000 – 5000/2 = 8500 Hz

## Slide 14
Figure 5.5 Solution to Example 5

## Slide 15: Frequency Shift Keying
In FSK , the frequency of the carrier signal is varied to represent binary 1 and 0.
The frequency of the signal duration is constant and its value depends on the bit (0 and 1) : both peak amplitude and phase remain constant.
FSK avoids most of the problems from noise. Because the receiving device is looking for specific frequency changes over a given number of periods, it can ignore voltage spikes.
The limiting factors of FSK are the physical capabilities of the carrier.

## Slide 16
Figure 5.6 FSK

## Slide 17
Figure 5.7 Relationship between baud rate and bandwidth in FSK

## Slide 18
Example 6
Find the minimum bandwidth for an FSK signal transmitting at 2000 bps. Transmission is in half-duplex mode, and the carriers are separated by 3000 Hz.
Solution
For FSK
BW = baud rate + fc1  fc0
BW = bit rate + fc1  fc0 = 2000 + 3000 = 5000 Hz

## Slide 19
Example 7
Find the maximum bit rates for an FSK signal if the bandwidth of the medium is 12,000 Hz and the difference between the two carriers is 2000 Hz. Transmission is in full-duplex mode.
Solution
Because the transmission is full duplex, only 6000 Hz is allocated for each direction.
BW = baud rate + fc1  fc0
Baud rate = BW  (fc1  fc0 ) = 6000  2000 = 4000
But because the baud rate is the same as the bit rate, the bit rate is 4000 bps.

## Slide 20: Phase Shift Keying
In PSK, the phase of the carrier is varied to represent binary 1 or 0.
Both peak amplitude and frequency remain constant as the phase changes.

## Slide 21
Figure 5.8 PSK

## Slide 22
Figure 5.9 PSK constellation

## Slide 23
Figure 5.10 The 4-PSK method

## Slide 24
Figure 5.11 The 4-PSK characteristics

## Slide 25
Figure 5.12 The 8-PSK characteristics

## Slide 26
Figure 5.13 Relationship between baud rate and bandwidth in PSK

## Slide 27
Example 8
Find the bandwidth for a 4-PSK signal transmitting at 2000 bps. Transmission is in half-duplex mode.
Solution
For PSK the baud rate is the same as the bandwidth, which means the baud rate is 5000. But in 8-PSK the bit rate is 3 times the baud rate, so the bit rate is 15,000 bps.

## Slide 28
Example 9
Given a bandwidth of 5000 Hz for an 8-PSK signal, what are the baud rate and bit rate?
Solution
For PSK the baud rate is the same as the bandwidth, which means the baud rate is 5000. But in 8-PSK the bit rate is 3 times the baud rate, so the bit rate is 15,000 bps.

## Slide 29
Quadrature amplitude modulation is a combination of ASK and PSK so that a maximum contrast between each signal unit (bit, dibit, tribit, and so on) is achieved.
Note:

## Slide 30
Figure 5.14 The 4-QAM and 8-QAM constellations

## Slide 31
Figure 5.15 Time domain for an 8-QAM signal

## Slide 32
Figure 5.16 16-QAM constellations

## Slide 33
Figure 5.17 Bit and baud

## Slide 34
Table 5.1 Bit and baud rate comparison
Modulation | Units | Bits/Baud | Baud rate | Bit Rate
ASK, FSK, 2-PSK | Bit | 1 | N | N
4-PSK, 4-QAM | Dibit | 2 | N | 2N
8-PSK, 8-QAM | Tribit | 3 | N | 3N
16-QAM | Quadbit | 4 | N | 4N
32-QAM | Pentabit | 5 | N | 5N
64-QAM | Hexabit | 6 | N | 6N
128-QAM | Septabit | 7 | N | 7N
256-QAM | Octabit | 8 | N | 8N

## Slide 35
Example 10
A constellation diagram consists of eight equally spaced points on a circle. If the bit rate is 4800 bps, what is the baud rate?
Solution
The constellation indicates 8-PSK with the points 45 degrees apart. Since 23 = 8, 3 bits are transmitted with each signal unit. Therefore, the baud rate is
4800 / 3 = 1600 baud

## Slide 36
Example 11
Compute the bit rate for a 1000-baud 16-QAM signal.
Solution
A 16-QAM signal has 4 bits per signal unit since
log216 = 4.
Thus,
(1000)(4) = 4000 bps

## Slide 37
Example 12
Compute the baud rate for a 72,000-bps 64-QAM signal.
Solution
A 64-QAM signal has 6 bits per signal unit since
log2 64 = 6.
Thus,
72000 / 6 = 12,000 baud

## Slide 38
5.2 Telephone Modems
Modem Standards

## Slide 39
A telephone line has a bandwidth of almost 2400 Hz for data transmission.
Note:

## Slide 40
Figure 5.18 Telephone line bandwidth

## Slide 41
Modem stands for modulator/demodulator.
Note:

## Slide 42
Figure 5.19 Modulation/demodulation

## Slide 43
Figure 5.20 The V.32 constellation and bandwidth
V.32 modem uses a combined modulation and encoding technique called
Trellis coded modulation.

## Slide 44
Figure 5.21 The V.32bis constellation and bandwidth

## Slide 45
Figure 5.22 Traditional modems

## Slide 46
Figure 5.23 56K modems

## Slide 47
5.3 Modulation of Analog Signals
Amplitude Modulation (AM)
Frequency Modulation (FM)
Phase Modulation (PM)

## Slide 48
Figure 5.24 Analog-to-analog modulation

## Slide 49
Figure 5.25 Types of analog-to-analog modulation

## Slide 50: AM
The bandwidth of AM signal is equal to twice the bandwidth of the modulation signal and covers a range centered on the carrier frequency.

## Slide 51
Figure 5.26 Amplitude modulation
The shaded portion of the graph is the frequency spectrum of the signal

## Slide 52
Figure 5.27 AM bandwidth

## Slide 53
Figure 5.28 AM band allocation

## Slide 54
Example 13
We have an audio signal with a bandwidth of 4 KHz. What is the bandwidth needed if we modulate the signal using AM? Ignore FCC regulations.
Solution
An AM signal requires twice the bandwidth of the original signal:
BW = 2 x 4 KHz = 8 KHz

## Slide 55: FM
In FM transmission the frequency of the carrier signal is modulation to follow the changing voltage level (amplitude) of the modulation signal. The peak amplitude and phase of the carrier signal remain constant but as the amplitude of the information signal changes, the frequency of the carrier changes correspondingly.

## Slide 56
Figure 5.29 Frequency modulation
Graph show the relationship of the modulation signal, the carrier signal,
and the resultant FM signal

## Slide 57
Figure 5.30 FM bandwidth

## Slide 58
Example 14
We have an audio signal with a bandwidth of 4 MHz. What is the bandwidth needed if we modulate the signal using FM? Ignore FCC regulations.
Solution
An FM signal requires 10 times the bandwidth of the original signal:
BW = 10 x 4 MHz = 40 MHz