## Slide 1
Chapter 10
Error Detection and Correction
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
Notes: <number>

## Slide 2
Data Link layer
Data link layer responsible for node-to-node (hop-to-hop) communication.
Specific responsibilities of the data link layer include framing, addressing, flow control, error control, and media access control.
Error control: Data link layer adds reliability to the physical layer by adding mechanisms to detect and retransmit damaged, duplicate, or lost frames.

## Slide 3
Data can be corrupted during transmission.
Some applications require that errors be detected and corrected.
Note
Notes: <number>

## Slide 4
Figure 10.1 Single-bit error
The term single-bit error means that only 1 bit of a given data unit is changed from 1 to 0 or from 0 to 1.
Single-bit errors are the least likely type of error in serial data transmission.

## Slide 5
A burst error means that 2 or more bits in the data unit have changed.
Note

## Slide 6
Figure 10.2 Burst error of length 8
The length of the burst is measured from the first corrupted bit to the last corrupted bit. Some bits in between may not have been corrupted.

## Slide 7
Redundancy
The central concept in detecting or correcting errors is redundancy.
To be able to detect or correct errors, we need to send some extra bits with our data.
These redundant bits are added by the sender and removed by the receiver.
Their presence allows the receiver to detect or correct corrupted bits.

## Slide 8
To detect or correct errors, we need to send extra (redundant) bits with data.
Note
Notes: <number>

## Slide 9
Coding
Redundancy is achieved through various coding schemes.
The sender adds redundant bits through a process that creates a relationship between the redundant bits and the
actual data bits.
The receiver checks the relationships between the two sets of bits to detect or correct the errors.
The ratio of redundant bits to the data bits and the robustness of the process are important factors in any coding scheme.

## Slide 10
Figure 10.3 The structure of encoder and decoder

## Slide 11
10-2 BLOCK CODING
In block coding, we divide our message into blocks, each of k bits, called datawords. We add r redundant bits to each block to make the length n = k + r. The resulting n-bit blocks are called codewords.
With k bits, we can create a combination of datawords; with n bits, we can create a combination of codewords.
Since n > k, the number of possible codewords is larger than the number of possible datawords.
The block coding process is one-to-one; the same dataword is always encoded as the same codeword.
This means that we have codewords that are not used. We call these codewords invalid or illegal.

## Slide 12
Figure 10.6 Process of error detection in block coding

## Slide 13
Error detection
If the following two conditions are met, the receiver can detect a change in the original codeword.
The receiver has (or can find) a list of valid codewords.
The original codeword has changed to an invalid one.
If the received codeword is the same as one of the valid codewords, the word is accepted; the corresponding dataword is extracted for use.
If the received codeword is not valid, it is discarded.
If the codeword is corrupted during transmission but the received word still matches a valid codeword, the error remains undetected.
This type of coding can detect only single errors. Two or more errors may remain undetected.

## Slide 14
An error-detecting code can detect only the types of errors for which it is designed; other types of errors may remain undetected.
Note

## Slide 15
Error correction
Error correction is much more difficult than error detection.
In error correction the receiver needs to find (or guess) the original codeword sent.
We need more redundant bits for error correction than for error detection.
Example 10.3

## Slide 16
Figure 10.7 Structure of encoder and decoder in error correction

## Slide 17
A simple parity-check code is a single-bit error-detecting code in which n = k + 1
Note
A simple parity-check code

## Slide 18
Table 10.3 Simple parity-check code C(5, 4): Even parity.

## Slide 19
Figure 10.10 Encoder and decoder for simple parity-check code
No error
error

## Slide 20
A simple parity-check code can detect an odd number of errors.
Note

## Slide 21
Figure 10.11 Two-dimensional parity-check code

## Slide 22
Figure 10.11 Two-dimensional parity-check code

## Slide 23
Figure 10.11 Two-dimensional parity-check code

## Slide 24
10-5 CHECKSUM
The last error detection method we discuss here is called the checksum. The checksum is used in the Internet by several protocols although not at the data link layer. However, we briefly discuss it here to complete our discussion on error checking

## Slide 25
Suppose our data is a list of five 4-bit numbers that we want to send to a destination. In addition to sending these numbers, we send the sum of the numbers. For example, if the set of numbers is (7, 11, 12, 0, 6), we send (7, 11, 12, 0, 6, 36), where 36 is the sum of the original numbers. The receiver adds the five numbers and compares the result with the sum. If the two are the same, the receiver assumes no error, accepts the five numbers, and discards the sum. Otherwise, there is an error somewhere and the data are not accepted.
Example 10.18

## Slide 26
We can make the job of the receiver easier if we send the negative (complement) of the sum, called the checksum. In this case, we send (7, 11, 12, 0, 6, −36). The receiver can add all the numbers received (including the checksum). If the result is 0, it assumes no error; otherwise, there is an error.
Example 10.19

## Slide 27
How can we represent the number 21 in one’s complement arithmetic using only four bits?
Solution
The number 21 in binary is 10101 (it needs five bits). We can wrap the leftmost bit and add it to the four rightmost bits. We have (0101 + 1) = 0110 or 6.
Example 10.20

## Slide 28
How can we represent the number −6 in one’s complement arithmetic using only four bits?
Solution
In one’s complement arithmetic, the negative or complement of a number is found by inverting all bits. Positive 6 is 0110; negative 6 is 1001. If we consider only unsigned numbers, this is 9. In other words, the complement of 6 is 9. Another way to find the complement of a number in one’s complement arithmetic is to subtract the number from 2n − 1 (16 − 1 in this case).
Example 10.21

## Slide 29
Let us redo Exercise 10.19 using one’s complement arithmetic. Figure 10.24 shows the process at the sender and at the receiver. The sender initializes the checksum to 0 and adds all data items and the checksum (the checksum is considered as one data item and is shown in color). The result is 36. However, 36 cannot be expressed in 4 bits. The extra two bits are wrapped and added with the sum to create the wrapped sum value 6. In the figure, we have shown the details in binary. The sum is then complemented, resulting in the checksum value 9 (15 − 6 = 9). The sender now sends six data items to the receiver including the checksum 9.
Example 10.22

## Slide 30
The receiver follows the same procedure as the sender. It adds all data items (including the checksum); the result is 45. The sum is wrapped and becomes 15. The wrapped sum is complemented and becomes 0. Since the value of the checksum is 0, this means that the data is not corrupted. The receiver drops the checksum and keeps the other data items. If the checksum is not zero, the entire packet is dropped.
Example 10.22 (continued)

## Slide 31
Figure 10.24 Example 10.22
1 0 0 1
1 1 1 1
0 0 0 0

## Slide 32
Internet Checksum
Sender site:
1. The message is divided into 16-bit words.
2. The value of the checksum word is set to 0.
3. All words including the checksum are added using one’s complement addition.
4. The sum is complemented and becomes the checksum.
5. The checksum is sent with the data.
Note

## Slide 33
Internet Checksum
Receiver site:
1. The message (including checksum) is divided into 16-bit words.
2. All words are added using one’s complement addition.
3. The sum is complemented and becomes the new checksum.
4. If the value of checksum is 0, the message is accepted; otherwise, it is rejected.
Note

## Slide 34
Let us calculate the checksum for a text of 8 characters (“Forouzan”). The text needs to be divided into 2-byte (16-bit) words. We use ASCII (see Appendix A) to change each byte to a 2-digit hexadecimal number. For example, F is represented as 0x46 and o is represented as 0x6F. Figure 10.25 shows how the checksum is calculated at the sender and receiver sites. In part a of the figure, the value of partial sum for the first column is 0x36. We keep the rightmost digit (6) and insert the leftmost digit (3) as the carry in the second column. The process is repeated for each column. Note that if there is any corruption, the checksum recalculated by the receiver is not all 0s. We leave this an exercise.
Example 10.23

## Slide 35
Figure 10.25 Example 10.23