## Slide 1
12.<number>
Chapter 12
Multiple Access
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
Notes: <number>

## Slide 2
12.<number>
Figure 12.1 Data link layer divided into two functionality-oriented sublayers
When nodes are connected and use a common link, called a multipoint or broadcast link, we need a multiple-access protocol to coordinate access to the link.
Notes: <number>

## Slide 3
12.<number>
Figure 12.2 Taxonomy of multiple-access protocols discussed in this chapter
Similar to the rules of speaking: guarantee that the right to speak, ensure that two people do not speak at the same time, do not interrupt each other, do not monopolize the discussion, and so on.
Notes: <number>

## Slide 4
12.<number>
12-1 RANDOM ACCESS
In random access or contention methods, no station is superior to another station and none is assigned the control over another. No station permits, or does not permit, another station to send. At each instance, a station that has data to send uses a procedure defined by the protocol to make a decision on whether or not to send.
Random access:
  No scheduled time for a station to transmit and
  No rules specify which station should send next.
Notes: <number>

## Slide 5
12.<number>
Figure 12.3 Frames in a pure ALOHA network
Even if one bit of a frame coexists on the channel with one bit from another frame, there is a collision and both will be destroyed.
Notes: <number>

## Slide 6
12.<number>
Pure ALOHA network
Resend frames that have been destroyed during transmission.
When a station sends a frame, it expects an acknowledgment. If no acknowledgment after a time-out period, the station assumes that the frame (or acknowledgment) has been destroyed and resends the frame.
A collision involves two or more stations.
If all these stations try to resend their frames after the time-out, the frames will collide again.
Pure ALOHA dictates that when the time-out period passes, each station waits a random amount of time before resending its frame.
The randomness will help avoid more collisions. This time is called the back-off time TB.
After a maximum number of retransmission attempts Kmax a station must give up and try later.
Notes: <number>

## Slide 7
12.<number>
Figure 12.4 Procedure for pure ALOHA protocol
Notes: <number>

## Slide 8
12.<number>
The stations on a wireless ALOHA network are a maximum of 600 km apart. If we assume that signals propagate at 3 × 108 m/s, we find
Tp = (6× 105 ) / (3 × 108 ) = 2 ms.
Now we can find the value of TB for different values of K .
a. For K = 1, the range is {0, 1}. The station needs to| generate a random number with a value of 0 or 1. This means that TB is either 0 ms (0 × 2) or 2 ms (1 × 2), based on the outcome of the random variable.
Example 12.1
Notes: <number>

## Slide 9
12.<number>
b. For K = 2, the range is {0, 1, 2, 3}. This means that TB can be 0, 2, 4, or 6 ms, based on the outcome of the random variable.
c. For K = 3, the range is {0, 1, 2, 3, 4, 5, 6, 7}. This means that TB can be 0, 2, 4, . . . , 14 ms, based on the outcome of the random variable.
d. We need to mention that if K > 10, it is normally set to 10.
Example 12.1 (continued)
Notes: <number>

## Slide 10
12.<number>
Vulnerable time: ALOHA
Vulnerable time
It is length of the time in which there is a possibility of collision.
The vulnerable time for pure ALOHA is 2 x Tfr.
Notes: <number>

## Slide 11
12.<number>
Figure 12.5 Vulnerable time for pure ALOHA protocol
A station may send soon after another station has started or soon before another station has finished.
Notes: <number>

## Slide 12
12.<number>
A pure ALOHA network transmits 200-bit frames on a shared channel of 200 kbps. What is the requirement to make this frame collision-free?
Example 12.2
Solution
Average frame transmission time Tfr is 200 bits/200 kbps or 1 ms. The vulnerable time is 2 × 1 ms = 2 ms. This means no station should send later than 1 ms before this station starts transmission and no station should start sending during the one 1-ms period that this station is sending.
Notes: <number>

## Slide 13
12.<number>
The throughput for pure ALOHA is S = G × e −2G .
The maximum throughput
Smax = 0.184 when G= (1/2).
Note
G the average number of frames generated by the system during one frame transmission time.
Notes: <number>

## Slide 14
12.<number>
A pure ALOHA network transmits 200-bit frames on a shared channel of 200 kbps. What is the throughput if the system (all stations together) produces
a. 1000 frames per second b. 500 frames per second
c. 250 frames per second.
Example 12.3
Solution
The frame transmission time is 200/200 kbps or 1 ms.
a. If the system creates 1000 frames per second, this is 1 frame per millisecond. The load is 1. In this case S = G× e−2 G or S = 0.135 (13.5 percent). This means that the throughput is 1000 × 0.135 = 135 frames. Only 135 frames out of 1000 will probably survive.
Notes: <number>

## Slide 15
12.<number>
Example 12.3 (continued)
b. If the system creates 500 frames per second, this is (1/2) frame per millisecond. The load is (1/2). In this case S = G × e −2G or S = 0.184 (18.4 percent). This means that the throughput is 500 × 0.184 = 92 and that only 92 frames out of 500 will probably survive. Note that this is the maximum throughput case, percentagewise.
c. If the system creates 250 frames per second, this is (1/4)frame per millisecond. The load is (1/4). In this case S = G × e −2G or S = 0.152 (15.2 percent). This means that the throughput is 250 × 0.152 = 38. Only 38 frames out of 250 will probably survive.
Notes: <number>

## Slide 16
12.<number>
Slotted ALOHA
More efficient than pure ALOHA
In slotted ALOHA, the time slots are divided into slots of Tfr, and the stations are forced to send their frames only at the beginning of the time slot.
Collisions are expected if two stations try to send at the beginning of the same time slot.
The vulnerable time is reduced to Tfr
Notes: <number>

## Slide 17
12.<number>
Figure 12.6 Frames in a slotted ALOHA network
If a station misses the beginning of this slot, it must wait the next time slot. Collision: if two stations try to send at the beginning of the same time slot.
The vulnerable time is now reduced to one-half, equal to Tfr.
Notes: <number>

## Slide 18
12.<number>
The throughput for slotted ALOHA is S = G × e−G .
The maximum throughput Smax = 0.368 when G = 1.
Note
Notes: <number>

## Slide 19
12.<number>
Figure 12.7 Vulnerable time for slotted ALOHA protocol
Notes: <number>

## Slide 20
12.<number>
A slotted ALOHA network transmits 200-bit frames on a shared channel of 200 kbps. What is the throughput if the system (all stations together) produces
a. 1000 frames per second b. 500 frames per second
c. 250 frames per second.
Example 12.4
Solution
The frame transmission time is 200/200 kbps or 1 ms.
a. If the system creates 1000 frames per second, this is 1 frame per millisecond. The load is 1. In this case S = G× e−G or S = 0.368 (36.8 percent). This means that the throughput is 1000 × 0.0368 = 368 frames. Only 386 frames out of 1000 will probably survive.
Notes: <number>

## Slide 21
12.<number>
Example 12.4 (continued)
b. If the system creates 500 frames per second, this is (1/2) frame per millisecond. The load is (1/2). In this case S = G × e−G or S = 0.303 (30.3 percent). This means that the throughput is 500 × 0.0303 = 151. Only 151 frames out of 500 will probably survive.
c. If the system creates 250 frames per second, this is (1/4) frame per millisecond. The load is (1/4). In this case S = G × e −G or S = 0.195 (19.5 percent). This means that the throughput is 250 × 0.195 = 49. Only 49 frames out of 250 will probably survive.
Notes: <number>

## Slide 22
12.<number>
Carrier Sense Multiple Access: CSMA
CSMA method was developed to increase the performance by minimizing the chance of collision.
Here the station senses the medium before trying to use it.
CSMA requires each station to first listen the medium before sending.
CSMA principle is “ sense before transmit” or “listen before talk”.
CSMA can reduce the possibility of collision, but it cannot eliminate it.
Notes: <number>

## Slide 23
12.<number>
Figure 12.8 Space/time model of the collision in CSMA
Notes: <number>

## Slide 24
12.<number>
Figure 12.9 Vulnerable time in CSMA
Notes: <number>

## Slide 25
12.<number>
Behavior of three persistence methods
Persistence methods
  Devises the behavior of a station, when a station is busy or idle.
  Three persistent methods are 1-persistent, nonpersistent and p-persistent.
Notes: <number>

## Slide 26
12.<number>
1-Persistent methods
Sense the channel.
– If busy, keep listening to the channel and
transmit immediately when the channel
becomes idle.
– If idle, transmit a packet immediately.
• If collision occurs,
– Wait a random amount of time and start over
again.
Notes: <number>

## Slide 27
12.<number>
Nonpersistent methods
Sense the channel.
– If busy, wait a random amount of time and sense the
channel again
– If idle, transmit a packet immediately
• If collision occurs
– wait a random amount of time and start all over again
Notes: <number>

## Slide 28
12.<number>
p-Persistent methods
If the medium is idle, transmit with probability p, and delay for one time unit with probability (1 - p)
(time unit = length of propagation delay)
If the medium is busy, continue to listen until medium becomes idle, then go to Step 1.
If transmission is delayed by one time unit, continue with Step 1
Notes: <number>

## Slide 29
12.<number>
Figure 12.12 Collision of the first bit in CSMA/CD
Carrier sense multiple access with collision detection (CSMA/CD) augments the algorithm to handle the collision.
Notes: <number>

## Slide 30
12.<number>
Figure 12.13 Collision and abortion in CSMA/CD
Notes: <number>

## Slide 31
12.<number>
Minimum Frame Size
Worst case time to detect collision is 2 propagation time:
  Frames should be long enough to allow collision detection prior to the end of transmission, otherwise CSMA/CD degrades to CSMA
Notes: <number>

## Slide 32
12.<number>
A network using CSMA/CD has a bandwidth of 10 Mbps. If the maximum propagation time (including the delays in the devices and ignoring the time needed to send a jamming signal, as we see later) is 25.6 μs, what is the minimum size of the frame?
Example 12.5
Solution
The frame transmission time is Tfr = 2 × Tp = 51.2 μs. This means, in the worst case, a station needs to transmit for a period of 51.2 μs to detect the collision. The minimum size of the frame is 10 Mbps × 51.2 μs = 512 bits or 64 bytes. This is actually the minimum size of the frame for Standard Ethernet.
Notes: <number>

## Slide 33
12.<number>
Figure 12.14 Flow diagram for the CSMA/CD
Notes: <number>

## Slide 34
12.<number>
Figure 12.15 Energy level during transmission, idleness, or collision
Notes: <number>

## Slide 35
12.<number>
CSMA/CA
In wireless networks collisions cannot be detected, so we use THREE strategies to avoid collisions .
1- Interframe space (IFS)
2- Contention window (CW)
3- Acknowledgement

## Slide 36
12.<number>
CSMA/CA
In wireless networks collisions cannot be detected, so we use THREE strategies to avoid collisions .
1- Interframe space (IFS): after sensing the channel idle, the station must wait an IFS period because there may be some remote station already started sending. If the channel is still idle after IFS waiting, the station can proceed to the next strategy.

## Slide 37
12.<number>
CSMA/CA
In wireless networks collisions cannot be detected, so we use THREE strategies to avoid collisions .
2- Contention window (CW): This is to randomize the waiting time of each station if more than one station has passed the same IFS waiting. In this case the station that will wait less in the CW will start transmission before all others, and the others will detect that and refrain from transmitting.

## Slide 38
12.<number>
CSMA/CA
In wireless networks collisions cannot be detected, so we use THREE strategies to avoid collisions .
3- Acknowledgement: If the sending station receives an acknowledgement within a specified time-out period the transmission is considered successful, otherwise the station will back-off and try again.

## Slide 39
12.<number>
Figure 12.16 Timing in CSMA/CA
Notes: <number>

## Slide 40
12.<number>
In CSMA/CA, the IFS can also be used to define the priority of a station or a frame.
Note
Notes: <number>

## Slide 41
12.<number>
In CSMA/CA, if the station finds the channel busy, it does not restart the timer of the contention window;
it stops the timer and restarts it when the channel becomes idle.
Note
Notes: <number>

## Slide 42
12.<number>
Figure 12.17 Flow diagram for CSMA/CA
Notes: <number>

## Slide 43
12.<number>
12-2 CONTROLLED ACCESS
In controlled access, the stations consult one another to find which station has the right to send. A station cannot send unless it has been authorized by other stations. We discuss three popular controlled-access methods:
  Reservation
  Polling
  Token Passing
Notes: <number>

## Slide 44
12.<number>
Figure 12.18 Reservation access method
In the reservation method, a station needs to make a reservation before sending data.
N stations : N reservation minislots in the reservation frame.
Each minislot belongs to a station.
When a station needs to send a data frame, it makes a reservation in its own minislot.
The stations that have made reservations can send their data frames after the reservation frame
Notes: <number>

## Slide 45
12.<number>
Polling access method
One device is designated as a primary station and the other devices are secondary stations.
All data exchanges must be made through the primary device even when the ultimate destination is a secondary device.
The primary device controls the link; the secondary devices follow its instructions.
It is up to the primary device to determine which device is allowed to use the channel at a given time.
If the primary wants to receive data, it asks the secondaries if they have anything to send; this is called poll function.
If the primary wants to send data, it tells the secondary to get ready to receive; this is called select function.
Notes: <number>

## Slide 46
12.<number>
Figure 12.19 Select and poll functions in polling access method
Notes: <number>

## Slide 47
12.<number>
Token-passing access method
Stations in a network are organized in a logical ring.
For each station, there is a predecessor and a successor.
A special packet called a token circulates through the ring. The possession of the token gives the station the right to access the channel and send its data.
When a station has some data to send, it waits until it receives the token from its predecessor.
It then holds the token and sends its data.
When the station has no more data to send, it releases the token, passing it to the next logical station in the ring.
Stations must be limited in the time they can have possession of the token.
The token must be monitored to ensure it has not been lost or destroyed.
Notes: <number>

## Slide 48
12.<number>
Figure 12.20 Logical ring and physical topology in token-passing access method
Notes: <number>

## Slide 49
12.<number>
12-3 CHANNELIZATION
Channelization is a multiple-access method in which the available bandwidth of a link is shared in time, frequency, or through code, between different stations. In this section, we discuss three channelization protocols.
Notes: <number>

## Slide 50
12.<number>
Frequency-division multiple access (FDMA)
The available bandwidth is divided into frequency bands.
Each station is allocated a band to send its data: each band is reserved for a specific station, and it belongs to the station all the time.
To prevent station interferences, the allocated bands are separated from one another by small guard bands.
FDMA, FDM (frequency division multiplexing) are different.
Notes: <number>

## Slide 51
12.<number>
Figure 12.21 Frequency-division multiple access (FDMA)
Notes: <number>

## Slide 52
12.<number>
In FDMA, the available bandwidth of the common channel is divided into bands that are separated by guard bands.
Note
Notes: <number>

## Slide 53
12.<number>
Time-division multiple access (TDMA)
The stations share the bandwidth of the channel in time.
Each station is allocated a time slot during which it can send data.
Each station transmits its data in is assigned time slot.
The main problem with TDMA lies in achieving synchronization between the different stations.
Each station needs to know the beginning of its slot and the location of its slot.
TDMA and TDM (time division multiplexing) are different
Notes: <number>

## Slide 54
12.<number>
Figure 12.22 Time-division multiple access (TDMA)
Notes: <number>

## Slide 55
12.<number>
In TDMA, the bandwidth is just one channel that is timeshared between different stations.
Note
Notes: <number>

## Slide 56
12.<number>
Code Division Multiple Access (CDMA)
12.<number>
In CDMA, one channel carries all transmissions simultaneously.
Note
CDMA differs from FDMA because only one channel occupies the entire bandwidth of the link. It differs from TDMA because all stations can send data simultaneously, no timesharing.
Notes: <number>

## Slide 57
12.<number>
Figure 12.23 Simple idea of communication with code
Notes: <number>

## Slide 58
12.<number>
Figure 12.24 Chip sequences
CDMA is based on coding theory. Each station is assigned a code, which is a sequence of numbers called chips.
We assume that the assigned codes have two properties:
1. If we multiply each code by another, we get 0.
2. If we multiply each code by itself, we get 4 (the number of stations).
Notes: <number>

## Slide 59
12.<number>
Figure 12.25 Data representation in CDMA
Rules for encoding: If a station needs to send a 0 bit, it encodes it as -1; if it needs to send a 1 bit, it encodes it as +1. When a station is idle, it sends no signal, which is interpreted as a 0.
Notes: <number>

## Slide 60
12.<number>
Figure 12.26 Sharing channel in CDMA
Notes: <number>

## Slide 61
12.<number>
Figure 12.27 Digital signal created by four stations in CDMA
Notes: <number>

## Slide 62
12.<number>
Figure 12.28 Decoding of the composite signal for one in CDMA
Notes: <number>

## Slide 63
12.<number>
Figure 12.29 General rule and examples of creating Walsh tables
Notes: <number>

## Slide 64
12.<number>
The number of sequences in a Walsh table needs to be N = 2m.
Note
Notes: <number>

## Slide 65
12.<number>
Find the chips for a network with
a. Two stations b. Four stations
Example 12.6
Solution
We can use the rows of W2 and W4 in Figure 12.29:
a. For a two-station network, we have [+1 +1] and [+1 −1].
b. For a four-station network we have [+1 +1 +1 +1], [+1 −1 +1 −1], [+1 +1 −1 −1], and [+1 −1 −1 +1].
Notes: <number>

## Slide 66
12.<number>
What is the number of sequences if we have 90 stations in our network?
Example 12.7
Solution
The number of sequences needs to be 2m. We need to choose m = 7 and N = 27 or 128. We can then use 90 of the sequences as the chips.
Notes: <number>

## Slide 67
12.<number>
Prove that a receiving station can get the data sent by a specific sender if it multiplies the entire data on the channel by the sender’s chip code and then divides it by the number of stations.
Example 12.8
Solution
Let us prove this for the first station, using our previous four-station example. We can say that the data on the channel D = (d1 ⋅ c1 + d2 ⋅ c2 + d3 ⋅ c3 + d4 ⋅ c4). The receiver which wants to get the data sent by station 1 multiplies these data by c1.
Notes: <number>

## Slide 68
12.<number>
Example 12.8 (continued)
When we divide the result by N, we get d1 .
Notes: <number>