## Slide 1: What Is Layout Planning?
Layout planning is deciding the best physical arrangement of all resources within a facility
Facility resource arrangement can significantly affect productivity
Two broad categories of operations:
  Intermittent processing systems – low volume of many different products
  Continuous processing systems – high volume of a few standardized products

## Slide 2: Types of Layouts
Four basic layout types consisting of:
  Process layouts - Group similar resources together
  Product layouts - Designed to produce a specific product efficiently
  Hybrid layouts - Combine aspects of both process and product layouts
  Fixed-Position layouts - Product is two large to move; e.g. a building

## Slide 3: Process Layouts
Process layout unique characteristics include:
  Resources used are general purpose
  Facilities are less capital intensive
  Facilities are more labor intensive
  Resources have greater flexibility
  Processing rates are slower
  Material handling costs are higher

## Slide 4: Process Layouts – con’t
Scheduling resources & work flow is more complex
Space requirements are higher

## Slide 5: Product Layouts
Product layout unique characteristics are:
  Resources are specialized
  Facilities are capital intensive
  Processing rates are faster
  Material handling costs are lower
  Space requirements for inventory storage are lower
  Flexibility is low relative to the market

## Slide 6: Process vs. Product Layouts
  Here are the characteristic differences between a process and product layout.

## Slide 7: Hybrid Layouts
Combine elements of both product & process layouts
  Maintain some of the efficiencies of product layouts
  Maintain some of the flexibility of process layouts
Examples:
  Group technology & manufacturing cells
  Grocery stores

## Slide 8: Fixed-Position Layout
Used when product is large
Product is difficult or impossible to move, i.e. very large or fixed
All resources must be brought to the site
Scheduling of crews and resources is a challenge

## Slide 9: Designing Process Layouts
Step 1: Gather information:
  Space needed, space available, identify closeness measures
Step 2: Develop alternative block plans:
  Using trial-and-error or decision support tools
Step 3: Develop a detailed layout:
  Consider exact sizes/shapes of departments and work centers including aisles and stairways
  Tools like drawings, 3-D models, and CAD software are available to facilitate this process

## Slide 10: Special Cases of Process Layouts
A number of unique process layouts require special attention. We will look at two of these:
Warehouse layouts
Office Layouts

## Slide 11: Warehouse Layouts
Warehouse Layout Considerations:
  Primary decision is where to locate each department relative to the dock
  Departments can be organized to minimize “ld” totals
  Departments of unequal size require modification of the typical ld calculations to include a calculation of the “ratio of trips to area needed”
  The usage of “Crossdocking” modifies the traditional warehouse layouts; more docks, less storage space, and less order picking

## Slide 12: Office Layouts
Office Layout Considerations:
  Almost half of US workforce works in an office environment
  Human interaction and communication are the primary factors in designing office layouts
  Layouts need to account for physical environment and psychological needs of the organization
  One key layout trade-off is between proximity and privacy
  Open concept offices promote understanding & trust
  Flexible layouts incorporating “office landscaping” help to solve the privacy issue in open office environments

## Slide 13: Designing Product Layouts
Designing product layouts requires consideration of:
  Sequence of tasks to be performed by each workstation
  Logical order
  Speed considerations – line balancing

## Slide 14: Designing Product Layouts – con’t
Step 1: Identify tasks & immediate predecessors
Step 2: Determine output rate
Step 3: Determine cycle time
Step 4: Compute the Theoretical Minimum number of Stations
Step 5: Assign tasks to workstations (balance the
line)
Step 6: Compute efficiency, idle time & balance delay

## Slide 15: Step 1: Identify Tasks & Immediate Predecessors

## Slide 16: Layout Calculations
Step 2: Determine output rate
  Vicki needs to produce 60 pizzas per hour
Step 3: Determine cycle time
  The amount of time each workstation is allowed to complete its tasks
  Limited by the bottleneck task (the longest task in a process):

## Slide 17: Layout Calculations con’t
Step 4: Compute the theoretical minimum number of stations
  TM = number of stations needed to achieve 100% efficiency (every second is used)
  Always round up (no partial workstations)
  Serves as a lower bound for our analysis

## Slide 18: Group Technology (CELL) Layouts
One of the most popular hybrid layouts uses Group Technology (GT) and a cellular layout
GT has the advantage of bringing the efficiencies of a product layout to a process layout environment

## Slide 19: Facility Layout Across the Organization
Layout planning is organizationally important for an efficient operations
  Marketing is affected by layout especially when clients come to the site
  Human resources is affected as layout impacts people
  Finance is involved as layout changes can be costly endeavors