## Slide 1: Networking & Internetworking
Connecting People, Places, and Everything Else

## Slide 2: Networks
Any connection between two or more computers
  e.g. Even when you connect two computers via a USB cable
Networks use a set of low-level protocols (rules for communication)
  e.g. TCP/IP, IPX/SPX (Internetwork Packet Exchange/Sequenced Packet Exchange)
Networks use standardized hardware
  e.g. Twisted pair cabling & Ethernet hubs, ATM switches & optical fibre cabling

## Slide 3: Network Speed
A network’s speed can be summed up with two values:
  Bit rate:
    How many bits can be placed on the network in a given time interval (e.g. 1 second)?
    This is often called bandwidth, but this is a misnomer since bandwidth has to do with the range of frequencies to be used
    Bit rate becomes the dominant factor when sending many packets (e.g. a large file)
  Latency:
    How long does it take a bit to be received by the destination node?
    Latency becomes the dominant factor when sending individual packets, or alternating sending/receiving

## Slide 4: A Local Area Network (LAN)

## Slide 5: Networks: Purpose
Sharing files
  FTP, NFS, SMB(server message block)
Communicating
  E-Mail, instant messaging, games
Executing programs remotely
  rlogin, telnet

## Slide 6: Network Messaging
Most local area networks use electrostatic network hardware
  The wires transmit messages using electricity
  The transmission hardware charges the wire positively or negatively to indicate 1 and 0 respectively
  The reception hardware senses the charge

## Slide 7: Internetworking: internets (WANs)
e.g. The Internet
Any connection between two or more networks
  e.g. An Ethernet network connected to another Ethernet network by glass fibre cable and ATM switches

## Slide 8: An Internet
LAN A
LAN B
LAN C
LAN E
LAN D
Backbone A

## Slide 9: Internets: Purpose
Larger scope
  Access more shared files
  Communicate with more people
  Execute programs on more machines

## Slide 10: Network Properties
Networking Fundamentals for Specific Network Types

## Slide 11: Important Network Properties
Scope: A network should provide services to several applications
Scalability: A network should operate efficiently when deployed on a small-scale as well as on a large-scale
Robustness: A network should operate in spite of failures or lost data

## Slide 12: Important Network Properties
Self-Stabilization: A network, after a failure or other problem, should return to normal (or near normal) without human intervention
Autoconfigurability: A network should optimize its own parameters in order to achieve better performance
Safety: A network should prevent failures as well as prevent failures from affecting other areas of the network

## Slide 13: Important Network Properties
Configurability: A network’s parameters should be configurable to improve performance
Determinism: Two networks with identical conditions should yield identical results
Migration: It should be possible to add new features to a network without disruption of network service

## Slide 14: Network Usage
Ideally, the network usage should be maximized
  If network resources are unused, the network is not being used efficiently
  Unused network resources could be used to provide higher throughput to hosts
This typically becomes a problem in routing
  If all routers choose the single optimal path, some (less than optimal) regions of the network will be unused

## Slide 15: The Internet
The Information Age

## Slide 16: Internet History
A Condensed Timeline of Internet Development and Research Projects

## Slide 17: The Birth of Arpanet
Developed by ARPA (Advanced Research Projects Agency)
  A packet-switched network connecting a number of LANs, called Arpanet
  Used primarily for connecting the networks of the U.S. Government’s defense initiative (DARPA, which was a branch of the DoD)
  Became a useable internet in 1977

## Slide 18: The Internet Split
Originally, Arpanet was strictly military and defense-oriented
Arpanet was converted to use the new standard TCP/IP protocol set (1980)
The Defense Communication Agency (DCA) split Arpanet into two networks (1983):
  Arpanet: To be used for internetworking research projects
  Milnet: To be used strictly for military purposes

## Slide 19: A Military & University Internet
The University of California (at Berkeley) incorporated TCP/IP programming into its BSD UNIX operating system (1983)
  ARPA funded research projects at many Universities in order to make then internet-capable (1983-1989)
  BSD UNIX developed the socket network programming model commonly used today
  It was now possible for anyone to write internet applications
    This resulted in a boom of internet applications, many of which survive to this day

## Slide 20: A Public Internet
It became practical for private organizations to connect to the Internet (mid-late 1980s)
  Due to inexpensive hardware
The Internet Architecture Board (IAB) was empowered to manage research
  Coordinates and focuses research and development with regards to the Internet and TCP/IP

## Slide 21: Internet Implementation
Under the Hood

## Slide 22: TCP/IP
A considerably large part of this course
The underlying network protocols upon which application-level protocols are built
  e.g. HTTP, SMTP, IMAP(Internet Message Access Protocol
TCP/IP is the framework for the Internet

## Slide 23: TCP/IP
TCP/IP is actually two protocols:
  TCP: Transport control protocol
    Creates reliable transport (handles lost messages), offers a logical stream of data (reorders mixed up messages)
  IP: Internet protocol
    Defines addressing (e.g. 137.207.32.2), routing protocols (how to get messages from source to destination), etc.

## Slide 24: Internet Messaging
TCP is a reliable protocol
  If a message does not arrive, it is re-sent
  Messages must be acknowledged by their recipients before a certain time expires
    The message’s time-to-live (TTL) value

## Slide 25: Layered Architectures
Schemes for Organizing the Responsibility of Networking Components

## Slide 26: Network Service Models
Provide a layered abstraction for networking
Each layer performs specific tasks
Between each layer is an interface
  e.g. The hardware access layer might interact directly with the hardware, providing a hardware-independent interface to higher layers
The same layer at the source and the destination are known as ‘peer’ layers
  e.g. A ‘transport’ layer may provide reliable messaging, so the transport layer in the source and destination will communicate to ensure each message arrived in tact

## Slide 27: Network Service Model
Sender
Receiver
Layer n
Layer n
…
…
Layer 2
Layer 2
Layer 1
Layer 1
Network
Lower level
Higher level

## Slide 28: The OSI Reference Model
A layered service model developed by the International Standardization Organization (ISO)
Defines 7 conceptual layers
  Each serves a very specific purpose
OSI: Open System Interconnection
Developed as a reference to be used for all future protocols

## Slide 29: The OSI Reference Model
The 7 layers are (highest to lowest level):
Application
Presentation
Session
Transport
Network
Data link
Physical

## Slide 30: The OSI Reference Model
Application
Application
Presentation
Presentation
Session
Session
Transport
Transport
Network
Network
Data link
Data link
Physical
Physical
protocol
protocol
protocol
protocol
protocol
protocol
protocol

## Slide 31: The OSI Reference Model
Represents the actual network hardware
Deals with problems such as:
  Sending signals across wires
    e.g. Charging a wire with a specific voltage
  Converting bits to signals
Even two Ethernet cards may have different physical layers, as this layer deals with hardware specific concerns
Physical Layer

## Slide 32: The OSI Reference Model
Represents the interface to the network hardware
Deals with problems such as:
  Transmission of groups of bits
    e.g. Groups of bits might represent an ASCII text string, a floating point number, or a chunk of binary data
  Verifying data integrity (using checksums)
Data Link Layer

## Slide 33: The OSI Reference Model
Handles the connection between sender and receiver
Deals with problems such as:
  Determining a path from the sender node to the recipient node (i.e. routing)
  Determining the correct recipient (i.e. addressing)
  Network congestion
  Fragmenting data into packets
  Reassembly of packets
Network Layer

## Slide 34: The OSI Reference Model
Represents an end-to-end reliable communication stream
Deals with problems such as:
  Lost (unacknowledged) packets
  Duplicate packets
  Reordering packets
Transport Layer

## Slide 35: The OSI Reference Model
Represents a dialogue between sender and receiver
Somewhat irrelevant in today’s networks
  Handles the establishment of an authenticated connection to the receiver
Deals with problems such as:
  Authentication of the sender node on the packet assembler and dissembler (PAD)
    This is a remote computer which provided the lower layers in a shared manner, which required authentication
Session Layer

## Slide 36: The OSI Reference Model
Specifies data representations so that both sides can determine how to read data
  e.g. How many bytes to use for floating point values (including compressed as well as uncompressed values, encryption)
  e.g. What is the order of the bytes?
  Uses an ISO-defined standard for these representations: Abstract Syntax Notation 1 (ASN.1)
Presentation Layer

## Slide 37: The OSI Reference Model
Defines what data is stored in the message (specific to each application)
  e.g. An E-Mail application would store such things as recipient, subject, and body text into an E-Mail application-level message
  e.g. A web server would put header information (information about the server & the document) as well as the document itself into its application-level messages
Application Layer

## Slide 38: OSI Reference Model: An Example
Session Message:
Session Header
Recipient
Subject
Body
Message:
Recipient – CHAR(9)
Subject – CHAR (17)
Body – CHAR (243)
Frame:
Data Link Header
Network Header
Transport Header
Session Header
Recipient
Subject
Body
Application
Presentation
Session
Transport
Network
Data link
Physical
E-Mail:
Recipient
Subject
Body
Network
01001101111010010011001…
Network Frame:
Network Header
Transport Header
Session Header
Recipient
Subject
Body
Transport Message:
Transport Header
Session Header
Recipient
Subject
Body
Notes: <number>
<footer>
<header>
<date/time>
The application layer has an E-Mail message to send.
When sent through the presentation layer, the data types are well defined for each component of the E-Mail message.
The session layer typically would do very little in modern networks.
The transport layer would add a message ID to the message, and set its time-to-live value. If an acknowledgement is not received by that time, the message will be reissued.
The network layer adds a recipient address as well as the sender’s address to the message. These addresses will be used by routers to direct the message through the correct path to the recipient. The network layer may also divide the message into smaller parts, called Frames, which are manageable by the network. Some networks have a maximum message size, some even have an exact length that all messages must be.
The data link layer issues commands to the network device to send the appropriate bytes.
The physical layer responds to these device commands and transmits a signal on the network wire. Which wires to charge, how, and how much are determined by the hardware and the type of network.

## Slide 39: OSI Reference Model: Routing
Application
Presentation
Session
Transport
Network
Data link
Physical
Application
Presentation
Session
Transport
Network
Data link
Physical
Network
Data link
Physical
Router
Notes: <number>
<footer>
<header>
<date/time>
The application layer has an E-Mail message to send.
When sent through the presentation layer, the data types are well defined for each component of the E-Mail message.
The session layer typically would do very little in modern networks.
The transport layer would add a message ID to the message, and set its time-to-live value. If an acknowledgement is not received by that time, the message will be reissued.
The network layer adds a recipient address as well as the sender’s address to the message. These addresses will be used by routers to direct the message through the correct path to the recipient. The network layer may also divide the message into smaller parts, called Frames, which are manageable by the network. Some networks have a maximum message size, some even have an exact length that all messages must be.
The data link layer issues commands to the network device to send the appropriate bytes.
The physical layer responds to these device commands and transmits a signal on the network wire. Which wires to charge, how, and how much are determined by the hardware and the type of network.

## Slide 40: OSI Reference Model Overview
Each layer provides some abstraction to the higher levels
  e.g. The physical layer actually charges the wire
    Higher layers need not worry about how to charge the wire
  e.g. The transport layer ensures that message arrive
    Higher layers can assume that messages will arrive, and will not be lost
The OSI reference model was used as the basis for X.25 networks.

## Slide 41: The TCP/IP Service Model
Researchers developing the TCP/IP protocol suite also developed a layered reference model
The TCP/IP reference model consists of 5 layers
  3 software layers
  1 software & hardware layer
  1 hardware layer

## Slide 42: The TCP/IP Service Model
The 5 layers:
Application
Transport
Internet
Network Interface
Hardware

## Slide 43: The TCP/IP Service Model
Defines what data is stored in the message (specific to each application)
  e.g. An E-Mail application would store such things as recipient, subject, and body text into an E-Mail application-level message
  e.g. A web server would put header information (information about the server & the document) as well as the document itself into its application-level messages
Essentially, this layer is identical to the application layer in the OSI reference model
Application Layer

## Slide 44: The TCP/IP Service Model
Handles end-to-end communication
  Divides the data into manageable chunks of information (packets)
  Provides reliable communication
    Ensures that all packets are received
  Provides error-free communication
    Uses a checksum to verify data integrity
Implemented by the TCP protocol
  Transport control protocol
Transport Layer

## Slide 45: The TCP/IP Service Model
Handles communication between machines
  The path of a message is determined (routing)
  The destination of a message is determined (addressing)
Implemented by the IP protocol
  Internet protocol
Internet Layer

## Slide 46: The TCP/IP Service Model
Handles low level interaction with hardware
  Issues commands to the hardware to transmit a number of bits (1 or 0)
  Deals with hardware-specific concerns
Implemented by the device drivers for the hardware installed into the operating system
Essentially, this layer is identical to the data link layer in the OSI model
Network Interface Layer

## Slide 47: The TCP/IP Service Model
Actually transmits signals onto the network
Deals with issues such as:
  How to transmit signals (e.g. electrify the wire)
  How to detect problems (e.g. collisions)
Represents the actual network hardware
Essentially this layer is identical to the physical layer in the OSI model
Hardware Layer

## Slide 48: TCP/IP Service Model: Example
Application
Transport
Internet
Network
Interface
Hardware
Network
01001101111010010011001…
IP Datagrams:
IP Header
TCP Header
Data Bytes
Transport Packet:
TCP Header
Data Bytes
E-Mail:
Data Bytes
Network Frame:
IP Header
TCP Header
Data Bytes
Notes: <number>
<footer>
<header>
<date/time>
The application layer has an E-Mail message to send.
When sent through the presentation layer, the data types are well defined for each component of the E-Mail message.
The session layer typically would do very little in modern networks.
The transport layer would add a message ID to the message, and set its time-to-live value. If an acknowledgement is not received by that time, the message will be reissued.
The network layer adds a recipient address as well as the sender’s address to the message. These addresses will be used by routers to direct the message through the correct path to the recipient. The network layer may also divide the message into smaller parts, called Frames, which are manageable by the network. Some networks have a maximum message size, some even have an exact length that all messages must be.
The data link layer issues commands to the network device to send the appropriate bytes.
The physical layer responds to these device commands and transmits a signal on the network wire. Which wires to charge, how, and how much are determined by the hardware and the type of network.

## Slide 49: TCP/IP Service Model: Routing
Application
Transport
Internet
Network
Interface
Hardware
Application
Transport
Internet
Network
Interface
Hardware
Internet
Network
Interface
Hardware
Router
Notes: <number>
<footer>
<header>
<date/time>
The application layer has an E-Mail message to send.
When sent through the presentation layer, the data types are well defined for each component of the E-Mail message.
The session layer typically would do very little in modern networks.
The transport layer would add a message ID to the message, and set its time-to-live value. If an acknowledgement is not received by that time, the message will be reissued.
The network layer adds a recipient address as well as the sender’s address to the message. These addresses will be used by routers to direct the message through the correct path to the recipient. The network layer may also divide the message into smaller parts, called Frames, which are manageable by the network. Some networks have a maximum message size, some even have an exact length that all messages must be.
The data link layer issues commands to the network device to send the appropriate bytes.
The physical layer responds to these device commands and transmits a signal on the network wire. Which wires to charge, how, and how much are determined by the hardware and the type of network.

## Slide 50: TCP/IP Service Model: Overview
Major differences between OSI and TCP/IP:
  TCP/IP has no presentation layer
    The applications must agree on a data format (how many bytes for a floating point, etc)
    Thus, presentation/encoding is handled by the application layer
  TCP/IP has no session layer
    Not significant: It does little in modern networks
    In TCP/IP a session is typically managed by the application layer

## Slide 51: The TCP/IP Protocol in Action
Consider the following simplified network route
  The source (S) and destination (D) are separated by two routers (R1, R2)
S
D
R1
R2

## Slide 52: The TCP/IP Protocol in Action
Let’s consider a web browser, using HTTP
  The web browser on S sends a packet to the web server on D
  The application layer (i.e. the browser) provides the logical (IP) addresses for S (IPS) and D (IPD)
  The application layer also provides the port numbers for the source (PortS) and destination (PortD)
S
D
R1
R2
HTTP Req

## Slide 53: The TCP/IP Protocol in Action
The Transport layer (TCP) uses the port numbers (e.g. 2765 and 80) to create a TCP packet (sometimes called a segment):
S
D
R1
R2
Source Port: 2765
Destination Port: 80
HTTP Req

## Slide 54: The TCP/IP Protocol in Action
Source IP: 137.207.140.71
Dest IP: 24.87.204.16
The Internet (i.e. IP) layer uses the IP addresses specified by the application layer to create an IP datagram
  e.g. 137.207.140.71, 24.87.204.16
  Next, a route is determined for the packet, using S’s routing table
    S only needs one router’s address (R1)
S
D
R1
R2
TCP Segment
HTTP Req

## Slide 55: The TCP/IP Protocol in Action
Source MAC: MACS
Dest MAC: MACR1
IP Datagram
The MAC addresses of S and R1 (MACS and MACR1) are used to create a network frame
  If the MAC address of R1 is not known, ARP (address resolution protocol) is used
S
D
R1
R2
TCP Segment
HTTP Req

## Slide 56: The TCP/IP Protocol in Action
Source MAC: MACS
Dest MAC: MACR1
IP Datagram
Let’s simplify the picture (for clarity)
  In subsequent steps the IP datagram and its contents will not change very much
S
D
R1
R2

## Slide 57: The TCP/IP Protocol in Action
Source MAC: MACS
Dest MAC: MACR1
IP Datagram
The network frame is transmitted on the network to R1
  This is possible since S and R1 are both members of the same network
S
D
R1
R2

## Slide 58: The TCP/IP Protocol in Action
IP Datagram
R1 will extract the IP datagram from the payload of the network frame
  R1 looks up the destination IP address (IPD) in it’s routing table, to determine which router should get the datagram next (R2)
S
D
R1
R2

## Slide 59: The TCP/IP Protocol in Action
Source MAC: MACR1
Dest MAC: MACR2
IP Datagram
R1 uses its own MAC address (MACR1) and R2’s MAC address (MACR2) to create another network frame
S
D
R1
R2

## Slide 60: The TCP/IP Protocol in Action
Source MAC: MACR1
Dest MAC: MACR2
IP Datagram
The network frame is received by R2, and the IP datagram is extracted from it’s payload
R2 uses its routing table to lookup IPD
  In this case, R2 is directly connected to D
    This is called direct routing
S
D
R1
R2

## Slide 61: The TCP/IP Protocol in Action
ARP Request
IP: 24.87.204.16
MAC: ?
IP Datagram
Most likely, R2 does not have the MAC address of D (MACD)
  The address resolution protocol (ARP) is used to determine the MAC address:
S
D
R1
R2

## Slide 62: The TCP/IP Protocol in Action
ARP Response
IP: 24.87.204.16
MAC: 08-7F-3C-90-0C-DF
IP Datagram
D recognizes it’s IP address and responds with its MAC address (MACD)
  e.g. 08-7F-3C-90-0C-DF
S
D
R1
R2

## Slide 63: The TCP/IP Protocol in Action
Source MAC: MACR2
Dest MAC: MACD
IP Datagram
A network frame is created by R2 now that the MAC address is known
The frame is sent directly to D
S
D
R1
R2

## Slide 64: The TCP/IP Protocol in Action
Source MAC: MACR2
Dest MAC: MACD
IP Datagram
D extracts the IP datagram from the network frame (which is discarded)
The IP datagram’s payload is passed to the transport layer
S
D
R1
R2

## Slide 65: The TCP/IP Protocol in Action
The Transport layer (within D’s operating system), will use the port numbers specified in the TCP segment to determine to which application it should send the segment
  In this case, to the application bound to port 80 (the web server)
S
D
R1
R2
Source Port: 2765
Destination Port: 80
HTTP Req

## Slide 66: The TCP/IP Protocol in Action
Now, the web server on D has the HTTP request, and it processes it
  An HTTP response is sent back using the same process
  The web server uses the same IP addresses and logical addresses as the last message
S
D
R1
R2
HTTP Req